## Slide 1: Datacenter as a Computer
Mosharaf Chowdhury

## Slide 2: Why is One Machine Not Enough?
Too much data
Too little storage capacity
Not enough I/O bandwidth
Not enough computing capability

## Slide 3: What’s in a Machine?
Interconnected compute and storage resources
  Different bandwidth and latency constraints
Simplified diagram
  Doesn’t include GPUs, accelerators such as FPGAs, faster networks such as RDMA, dedicated GPU interconnects such as NVlink, etc…
Memory Bus
Ethernet
SATA
PCIe v4
(1 GB/s)
(2 GB/s)*
(600 MB/s)*
(50 - 100 MB/s)*
(100 GB/s)
* Multiple channels

## Slide 4: Scale Up: Make More Powerful Machines
Moore’s law
  Stated 52 years ago by Intel founder Gordon Moore
  Number of transistors on microchip double every 2 years
  Today “closer to 2.5 years” – Intel CEO Brian Krzanich

## Slide 5: Dennard Scaling is the Problem
Suggested that power requirements are proportional to the area for transistors
  Both voltage and current being proportional to length
  Stated in 1974 by Robert H. Dennard (DRAM inventor)
Broken since 2005
“Adapting to Thrive in a New Economy of Memory Abundance,” Bresniker et al

## Slide 6: Dennard Scaling is the Problem
Performance per-core is stalled
Number of cores is increasing
“Adapting to Thrive in a New Economy of Memory Abundance,” Bresniker et al

## Slide 7: Storage Hierarchy
(https://www.youtube.com/watch?v=IWsjbqbkqh8)
L1 cache
L2 cache
L3 cache
RAM
3D Xpoint
SSD
HDD
Notes: 3D Xpoint
Few times slower reads than RAM
Writes are few times slower than reads
Non-volatile and byte-addressable
Interface is b/w-limited (6 GB/s)

## Slide 8: Scaling Up is Unlikely to Help
Physical limits
Economical constraints
What about fault-tolerance?
How would you upgrade?
Anything else?

## Slide 9: Scale Out: Warehouse-Scale Computers
Single organization
Homogeneity (to some extent)
Cost efficiency at scale
  Multiplexing across applications and services
  Rent it out!
Many concerns
  Infrastructure
  Networking
  Storage
  Software
  Power/Energy
  Failure/Recovery
  …

## Slide 10: Architectural Overview
Memory Bus
Ethernet
SATA
PCIe
Server
Server

## Slide 11: Power, Energy, Modeling, Building,…
Many challenges
We’ll focus primarily on software infrastructure in this class

## Slide 12: Datacenter Needs an Operating System
Datacenter is a collection of
  CPU cores
  Memory modules
  SSDs and HDDs
All connected by an interconnect
A computer is a collection of
  CPU cores
  Memory modules
  SSDs and HDDs
All connected by an interconnect

## Slide 13: Some Differences
High-level of parallelism
Diversity of workload
Resource heterogeneity
Failure is the norm
Communication dictates performance

## Slide 14: Three Categories of Software
Platform-level
  Software firmware that are present in every machine
Cluster-level
  Distributed systems to enable everything
Application-level
  User-facing applications built on top

## Slide 15: Common Techniques
Technique | Performance | Availability
Replication |  | 
Erasure coding |  | 
Sharding/partitioning |  | 
Load balancing |  | 
Health checks |  | 
Integrity checks |  | 
Compression |  | 
Eventual consistency |  | 
Centralized controller |  | 
Canaries |  | 
Redundant execution |  | 

## Slide 16: Common Techniques
Technique | Performance | Availability
Replication | X | X
Erasure coding | X | X
Sharding/partitioning | X | X
Load balancing | X | 
Health checks |  | X
Integrity checks |  | X
Compression | X | 
Eventual consistency | X | X
Centralized controller | X | 
Canaries |  | X
Redundant execution | X | 

## Slide 17: Datacenter Programming Models
Fault-tolerant, scalable, and easy access to all the distributed datacenter resources
  Users submit jobs to these models w/o having to worry about low-level details
MapReduce
  Grandfather of big data as we know today
  Two-stage, disk-based, network-avoiding
Spark
  Common substrate for diverse programming requirements
  Many-stage, memory-first

## Slide 18: Datacenter File Systems
Fault-tolerant, efficient access to data
GFS
  Data resides with compute resources
  Compute goes to data; hence, data locality
  The game changer: centralization isn’t too bad!
FDS
  Disaggregated storage (compute and storage are not collocated)
  Relies on full bisection bandwidth networks

## Slide 19: Datacenter “Operating Systems”
Fair and efficient distribution of resources among many competing programming models and jobs
  Does the dirty work so that users won’t have to
Borg
  Google’s cluster manager
  Utilization-first allocator
  Grand father of Kubernetes
Mesos / YARN
  Started with a simple question – how to run different versions of Hadoop?
  Fairness-first allocator

## Slide 20: Resource Allocation and Scheduling
How do we divide the resources anyway?
DRF
  Multi-resource max-min fairness
  Two-level; implemented in Mesos and YARN
  HUG: DRF + High utilization
  Carbyne: DRF + Altruism over complex DAGs

## Slide 21: Unavailability and Failure
In a 10000-server DC, with 10000-day MTBF machines, one machine will fail everyday on average
Build fault-tolerant software infrastructure and hide failure-handling complexity from application-level software as much as possible
Configuration is one of the largest sources of service disruption
Storage subsystems are the biggest sources of machine crashes
Tolerating/surviving from failures is different from hiding failures

## Slide 22
What’s the most critical resource in a datacenter?
Why?

## Slide 23: Break!

## Slide 24: Datacenter Networks
Memory Bus
Ethernet
SATA
PCIe
Server
Server

## Slide 25: Datacenter Networks
Traditional hierarchical topology
  Expensive
  Difficult to scale
  High oversubscription
  Smaller path diversity
  …
Core
Agg.
Edge

## Slide 26: Datacenter Networks
Clos topology
  Cheaper
  Easier to scale
  NO/low oversubscription
  Higher path diversity
  …
Core
Agg.
Edge

## Slide 27: Datacenter Topology: Clos aka Fat-tree
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines

## Slide 28: Datacenter applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 29: Partition-Aggregate
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 30: Partition-Aggregate
Mosharaf
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 31: Map-Reduce
Reduce Stage
Map Stage
The most popular software that follows this paradigm is Apache Spark

## Slide 32: Datacenter Traffic
Rack
Aggregation
Core
North-South Traffic
East-West Traffic

## Slide 33: East-West Traffic
Traffic between servers in the datacenter
Communication within “big data” computations
Traffic may shift on small timescales (< minutes)

## Slide 34: Datacenter Traffic Characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 35: What Do We Want?
Want to be able to run applications anywhere
Want to be able to migrate applications while they are running
Want to balance traffic across all these paths in the network
Want to fully utilize all the resources we have
…

## Slide 36: Using Multiple Paths Well

## Slide 37: Layer 2/Layer 3 Design Goals
Routing protocol must expose all available paths
Forwarding must spread traffic evenly over all paths

## Slide 38: Forwarding
Per-packet load balancing
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 39: Forwarding
Per-packet load balancing
  Traffic well spread (even w/ elephant flows)
  BUT Interacts poorly w/ TCP
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 40: Forwarding
Per-flow load balancing (ECMP, “Equal Cost Multi Path”)
  E.g., based on (src and dst IP and port)
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 41: Forwarding
Per-flow load balancing (ECMP)
  A flow follows a single path ( TCP is happy)
  Suboptimal load-balancing; elephants are a problem
to D
to D
to D
from A (to D)
from B (to D)
from C (to D)

## Slide 42: Solution 1: Topology-aware addressing
10.0.*.*
10.1.*.*
10.2.*.*
10.3.*.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 43: Solution 1: Topology-aware addressing
10.0.0.*
10.1.0.*
10.2.0.*
10.3.0.*
10.0.1.*
10.1.1.*
10.2.1.*
10.3.1.*
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 44: Solution 1: Topology-aware addressing
10.0.0.0
10.0.0.1
10.0.1.0
10.0.1.1
10.1.0.0
10.1.0.1
10.1.1.0
10.1.1.1
10.2.0.0
10.2.0.1
10.2.1.0
10.2.1.1
10.3.0.0
10.3.0.1
10.3.1.0
10.3.1.1
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 45: Solution 1: Topology-aware addressing
Addresses embed location in regular topology
Maximum #entries/switch: k ( = 4 in example)
  Constant, independent of #destinations!
No route computation / messages / protocols
  Topology is hard-coded, but still need localized link failure detection
Problems?
  VM migration: ideally, VM keeps its IP address when it moves
  Vulnerable to (topology/addresses) misconfiguration
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 46: Solution 2: Centralize + Source Routes
Centralized “controller” server knows topology and computes routes
Controller hands server all paths to each destination
  O(#destinations) state per server, but server memory cheap (e.g., 1M routes x 100B/route=100MB)
Server inserts entire path vector into packet header (“source routing”)
  E.g., header=[dst=D | index=0 | path={S5,S1,S2,S9}]
Switch forwards based on packet header
  index++; next-hop = path[index]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 47: Solution 2: Centralize + Source Routes
#entries per switch?
  None!
#routing messages?
  Akin to a broadcast from controller to all servers
Pro:
  Switches very simple and scalable
  Flexibility: end-points control route selection
Cons:
  Scalability / robustness of controller (SDN issue)
  Clean-slate design of everything
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 48: Upper Layer Networking
Layer 4 transport protocols
  DCTCP: Datacenter TCP
  Reacts to the actual extent of congestion instead of using binary feedback
Layer 7 application-aware protocols
  Coflow treats collections of flows between two computation stages together

## Slide 49: Open Discussion - 1
Will we come back to Shared-Everything model?
  Shared-Nothing: Datacenters
  Shared-Everything: Servers
If yes, why and when?
If not, why not?

## Slide 50: Shared-Something + Resource Disaggregation is Here!

## Slide 51: Open Discussion - 2
Will we come back to client-centric models?
  As opposed to server-centric/datacenter-driven model today
If yes, why and when?
If not, why not?

## Slide 52: Edge Computing + IoT is Here!
Diagram from https://www.openautomationsoftware.com

## Slide 53: Next Class…
Read the assigned papers
  Spark and FDS
Form groups of 3 and fill out https://forms.gle/YrrMqnWsBRFfcr9s8 by Jan 20
  This includes track and paper preference for your group